The PyBinaryClock

# Technical description
The circuit board is a type of 'hat' to a raspberry pi zero with 20 WS2812B programmable LEDs for the clock-display, a 2x20 header for the pi connection and a real-time clock circuit. The board was manufactured by https://aisler.net that has a great quality service for small series of prototypes.
The kit is mounted between two part of plexi-glass panels to make a clock that can be mounted on the wall or put on a table. See pictures below.
The code depend on https://github.com/rpi-ws281x/rpi-ws281x-python Install this first.
It is a very simple 'game-loop' kind of program that updates every 1/10 second. Taking current time and split to each figure (collumn) and then calculate the bit-pattern and set the LEDs accordingly.

## The hardware:
### Raspberry Pi zero
- Install rasbian light and configure it for your localization etc.
- Enable the I2C interface: https://www.raspberrypi-spy.co.uk/2014/11/enabling-the-i2c-interface-on-the-raspberry-pi/
- Install the RTC clock module software and set it up the properly. The hardware is already present on the circuit-board in a correct way: https://www.raspberrypi-spy.co.uk/2015/05/adding-a-ds3231-real-time-clock-to-the-raspberry-pi/
- Get the python lib for WS281x programmable leds: https://github.com/rpi-ws281x/rpi-ws281x-python
- Get the software for the binary clock from from github: https://github.com/teddycool/BinaryClock
- Fix autostart at boot, add these lines before 'exit' in /etc/rc.local
  - cd /home/pi/pybinaryclock
  - sudo python Main.py

### Binary display
Circuit board
Bill of material

## The PyBinaryClock software: